## Slide 1
OpenVPP Challenge · Software For Energy
EVs are underused grid + inference assets
One battery · three revenue streams · mobility never broken
• Every EV carries ~100 kWh of storage and sits idle 18–22 h per day.
• Arizona: ~10 major grid stress events per year; summer peaks stress AC load.
• Parked EVs can also host distributed inference — a second value stream.
• Core problem: allocate the same ~30–50 kWh of flexible energy across mobility, V2G, and inference — under uncertainty — without breaking trips.

## Slide 2
Approach
One orchestrator, three markets, every hour
• Per-vehicle rolling-horizon stochastic MILP — 24 h look-ahead, 1 h commit.
• Mobility enters as a dual price (λ $/h), not a hard constraint — the optimizer trades off lost trips against revenue and usually finds it's not worth it. Reliability emerges; it isn't hand-coded.
• Three-way co-optimization of charge · V2G · inference, against 5 joint scenarios drawn from seasonal event, LMP, and demand forecasters.
• Same solver for private and fleet-managed vehicles — parameters (λ, driving pattern) differ per-vehicle; the logic does not.
• No vehicle-to-vehicle coupling → N-way parallel. Fleet scale = N × per-vehicle cost / cores. Brief's 'thousands of vehicles' is a cluster config, not an architecture change.

## Slide 3
Technical approach
Stochastic MILP on seeded synthetic traces
• Signals: fleet, trips, LMP, grid events, inference demand — all parameter-calibrated from the challenge brief + ADOT, MAG, Argonne, ERCOT/CAISO sources.
• Forecasters: seasonal Bernoulli for grid events; AR(1) for LMP; Poisson for inference sessions.
• MILP: PuLP + CBC. ~200 variables, ~800 constraints per vehicle-day.
• Rolling horizon: replay the year hour-by-hour, solve a fresh 24 h LP every step, commit only t=0.
• 5 baselines: passive · smart-charge · V2G-only · greedy · stochastic.
• Sensitivity analysis: revenue vs. inference-price multiplier, 0× → 2×.
• Streamlit dashboard: live fleet map · event simulator · economics · baseline comparison. Reproducible from one command.
• Transparent assumptions: every derived parameter flagged + cited in `docs/assumptions.md`.

## Slide 4
Results
+$1,996 / vehicle / year · 100.0% mobility reliability
+195% above V2G-only · brief bands met across the board
• Event-window V2G: ~$83/yr (brief band $20–150 · in range).
• Inference revenue: $1,986/yr (brief band $750–3,000 · in range).
• Peak-arbitrage V2G: ~$2,782/yr — bonus value the brief didn't explicitly price but the optimizer found.
• Private vehicles: $2,122/yr · Fleet-managed: $1,700/yr. Same model handles both without per-segment tuning.
• Defensive proof: at 0× inference price, stochastic co-opt still beats V2G-only and smart-charge. Not a one-bet product.

## Slide 5
Roadmap
From brief-compliant prototype to pilot
• Real data: swap synthetic LMP / event traces for EIA-930 + utility TOU schedules; swap synthetic trips for anonymized telematics.
• Chance-constrained mobility: promote reliability from a soft penalty to a probabilistic guarantee (e.g., P[miss] ≤ 1% per driver).
• OpenVPP integration: expose the per-vehicle decision as a settlement API; stream decisions on a 5-min cadence instead of hourly.
• Fleet scale-out: horizontal scaling across cores / nodes; 10k vehicles in < 1 h for daily re-plan.
• Driver UX: an override dial so owners can trade earnings for slack (e.g., 'leave 80 kWh tonight, I'm going camping').